ZX Mega ULA
# Rationale
As an out of date chip is coming to the end of its life, even though some replacement is available, it might become necessary (more likely just good) that some specification for maximizing the potential replacement opportunity, even before failure. Even as an emulation expansion standard or in FPGA cores, it might increase the flexibility of tools and all things Z80 and ZX Spectrum. From servicing old equipment to bringing highly compatible but advanced features encouraging programming, development and thought.
# Options
- A plug in replacement. (already available).
- A plug in replacement with a video RAM replacement also onboard.
- Replacement with access to mainboard processor half address and data bus for full ROM/RAM replacement.
- Also with ED xx opcode co-processing for the Z80 at high speed. Requires /M1 signal.
- An on-board (perhaps turbo) Z80 removing the need to intercept the external Z80 bus.
- Extended graphics with excellent compatibility, but future and re-release software options.
- A SoC plus using the mainboard as just a power IO (port connectivity) and video mixer.
- On-board Z80 turbo and delegate Z80 (with appropriate ROM) for edge connector IO.
- ULA full feature plus auxiliary board for edge connector with Raspberry Pi GPIO exit on outside of auxiliary board. Allowing Pi HAT as expansion and intercept of mainboard Z80 bus.
- As last but replacing mainboard Z80 with the turbo on-board Z80 as edge connector driver. Jumper selectable? Bus cycle time on edge connector is important.
- A turbo extended ISA Z80 on-board with only the lower 32kB shared but with different ULA ROM (96kB total RAM, old ROM for mainboard). This makes edge connector issues easier. PREFERRED OPTION
# Why a Z80 as the Turbo Option
Easy availability of source assembler via `fuse` and other emulators. Keeping the same development tools might be important for developers. Not just another ARM system, but keeping the 8-bit low level, and restrictions on for challenging but in a sense simpler code development.
It’s an OK architecture with maybe too many specific cases like DJNZ compilers might not use, but is a good machine to learn assembly on. It requires less thinking like a compiler and more like a human without having to imagine 64-bit “typing” at the keyboard.
# Calculations GFX and General
Compatible but extended GFX is a Google Sheet with some calculations on hiding 16kB behind the ROM to extend the graphics mode so as to not matter if the shadow RAM behind the ROM is written as complete zero bytes.
# ED XX (2 Byte NOPs) Expansion Possibilities
M\L	0	1	2	3	4	5	6	7	8	9	A	B	C	D	E	F
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F

This is a lot of opcodes, but there are limits on using HL, IX and IY as ED cancels other prefixes in the standard Z80. If ED did not do this all three of the useful 16 bit registers would be open to use in these extensions. For easy decode things should not be made too complicated. As ED is already doing significant alteration of opcodes, while DD and FD are just doing some register exchange and addressing mode only changes, ED seems the best place to expand irregular operation behaviour.
# Repeated Extended NOP (1 to 3 Byte) Possibilities
M\L	DD (IX)	ED (XX)	FD (IY)
DD	IU Mode?	IX Mode?	IV Mode?
FD	IW Mode?	IY Mode?	IZ Mode?

These are harder to use, especially DD and FD following (on the right or least significant), unless 4 more index registers are considered on the turbo Z80. The ED following makes for 2 sets of 3 byte NOPs except where blacked out in the ED XX table above, unless the general principal to allow HL, IX and IY in ED instructions is allowed for effect and more indexing registers.
An alternate hardware Verilog source Z80 core adds the greyed out opcodes as duplicates and not NOPs. It also shows the many opcodes not affected by DD and FD as no HL register specification is included in their base opcode. An assembler is unlikely to generate them in prefixed form and so technically they would be 1 byte NOPs.
Keeping DD and FD as addressing mode operators might be an optimal solution until the ED space has run out of allocatable opcodes. DD DD ED XX could logically provide the ED in IU mode, and so on. Maybe it’s something about innovative use of index registers that makes for a good interpretation of how DD and FD are considered with other registers and opcodes. At least in some cases. Some opcodes may not be available for IU, IV, IW and IZ.
Considering superscalar designs might be taking it too far. Having four extra index registers is quite a pointer resource with a net reduction in code and data bandwidth waste via storage spill. It’s getting close to the RISC sweet spot of about eight to sixteen 16 bit registers.
# DD and FD Redundant NOPs before Ops (IX and IY Modes)
M\L	0	1	2	3	4	5	6	7	8	9	A	B	C	D	E	F
0
1
2
3
4
5
6
7
8
9
A
B
C
D
E
F

# ULA Port FE
Port Write FE
RST Z80	NMI Z80	EN Z80	Ear	Mic	Border

To reset the auxiliary Z80 the high bit is set. The NMI can also be triggered by a bit. The final “free” bit works as an enable (run) active high. All three are active low signals. Power on reset is automatic. The higher speed of this Z80 allows the line blanking to be connected to the /INT signal internally for higher speed synchronous programming. By default the /NMI can copy and/or pack or unpack data to or from the shared memory window to the unshared 32kB. The auxiliary Z80 IO ports are not visible from the mainboard Z80 programming model. To aid line interrupts /M1 and /IOREQ are used to place the video line pair number on the data bus. Zero is the first two graphical bitmap lines and then increases by two for easy interrupt mode IM 2 [0 .. 95] and the rest for the vertical blanking interval. BEEP and BORDER disable the auxiliary Z80 by design.
Port Read FE
/HALT	/TOUCH	Ear	Keyboard

The high bit reads as the HALT state of the auxiliary Z80, along with indicating still power on resetting and not enabled as a general not busy indication. The touch signal indicates if the lower 32kB has been written to by the auxiliary Z80 since the last read of port FE, which sets the bit again.

# Extended Graphics
By placing 16kB as write only RAM behind the ROM which is read only, an extra 2 graphical bit planes can be used along with 5 attribute planes (which are 8 bit). This gives an extended colour mode. The main graphics plane is the least significant bit. This arrangement allows easy compatibility when the shadow RAM is all zeros. BG and FG are alternated when the FLASH attribute is selected.
000	001	010	011	100	101	110	111
BG	FG	BORDER	AT4	AT0	AT1	AT2	AT3

This leaves 256 bytes for an audio engine waveform (8-bit samples). The wave is played cycled at a period of time set by ports FC (MSB) and FA (LSB). These can be read for the current counter indexed sample (FC) and current index fraction (FA). As the period counter is reached (a hidden register) the fraction is incremented. When the fraction carries, the sample index increments. This makes the mainboard Z80 responsible for deciding the note while the auxiliary Z80 being fast can modify the wave dynamically based on the horizontal blanking.
The attribute bytes are linearly laid out with content as follows in component intensity order.
Extended Attribute Byte
GREEN (3)	RED (3)	BLUE (2)

To remove the need for analogue circuitry on the ULA, four times oversampled bitstream 1-bit DACs can be used for video and audio. This sets an frequency minimum of 32MHz. An on-board (on chip) boost PLL can do this.
# The Step Debug Port
Port F9 on the mainboard Z80 sets the instruction to be presented on the data bus in interrupt mode 0. This allows a HALT and jump loop to execute single byte opcodes on the auxiliary Z80. Reads on the port provide the last executed instruction /M1 initial byte. A few gate to ED some things instead of XX confusions.
The F7 extended debug port cycles the colour of the border while F9 reads the same as F7 was set. It reads as the last instruction byte following byte after ED, DD or FD. This allows fancy detection of multi-byte codes. Remembering this system is all “kinda KIM-1”.
Well, enough of the tits up guru meditation “kids in America”, and onto the extension of the Z80 arch. “Manic Minercraft” wow “the impossible triangler” and the flux0nonathelon.
# Architecture Subroutines of Common Nature

# Notes
- Interrupt mode 1, key reading routine clobbers IY. Mode 2 requires ROM specifics or 257 byte table to routine (singular).
- A Z80 core in Verilog (A starting point)